## Slide 1: Nepal Flood & Weather Analysis
Predicting next-day river discharge and high-flow events with machine learning
Machine Learning Live Project | Anseena A S
Notes: This is my final internship project. I analysed daily weather and river-discharge records from 10 monitoring stations in Nepal, explored the patterns, and built models to predict next-day river discharge and to classify high-flow observations.

## Slide 2: Project introduction
Background
Floods are linked to heavy rainfall and rising river flow.
This project studies daily weather and river discharge records from 10 monitoring stations in Nepal.
Data period: 1 Jan 2023 to 31 Aug 2026.
Why monitoring matters
Rainfall and river discharge are key indicators for flood monitoring.
Tracking them shows seasonal patterns and differences between stations.
Past records can help models estimate future river discharge.
Regression task
Predict next-day river discharge (m³/s).
Classification task
Label high-flow observations using the same day's discharge. This is not a next-day forecast.
Notes: This slide gives the background. Rainfall and river discharge are the main measurements used to monitor flood conditions, so I used them to explore patterns and to build models. Two tasks: regression predicts tomorrow's discharge; classification labels a day as high flow using that same day's discharge, so it is not a forecast.

## Slide 3: Dataset and preprocessing
Location
Station, river and basin
Latitude, longitude, elevation
10 stations, 9 basin labels
Weather
Rain, precipitation, precipitation hours
Soil moisture
Temperature, dew point, humidity
Wind speed, gusts and direction
River
Daily discharge (m³/s)
1 Jan 2023 to 31 Aug 2026
19 original variables
Gaps from lag, rolling and next-day features filled with the mean
13,390
model-ready records (no rows dropped)
0
missing values and duplicates in the raw data
36
input features after feature creation and encoding
Notes: The raw data has 13,390 rows and 19 variables, with no missing values or duplicates. Creating lag, rolling and next-day features leaves some gaps at the start and end of each station's series. In the final notebook these gaps, including the next-day target, were filled with the column mean, so no rows were dropped. The notebook itself lists this as a limitation because it adds estimated values.

## Slide 4: River discharge is right-skewed
20.37
Mean (m³/s)
1.88
Median (m³/s)
84.33
Standard deviation (m³/s)
3,175.87
Maximum (m³/s)
The mean is above the 75th percentile, so a small number of very high values pull the average up. Most observations are low flow.
Chart: Discharge: percentiles and mean (m³/s)
| 25th percentile | Median | 75th percentile | Mean
Discharge | 0.26 | 1.88 | 10.53 | 20.37
Notes: This is why I report the median as well as the mean. The median is 1.88 m3/s but the mean is 20.37, and the maximum is 3,175.87. The distribution is strongly right-skewed.

## Slide 5: Discharge differs strongly by station
Chart: Average discharge by station (m³/s)
| Bhada Bridge | Chisapani | Rasuwagadhi | Chatara | Khokana | Devghat | Bahrabise | Chameliya/Nayalbadi | Belsot | Kusum
Avg discharge | 0.7 | 0.85 | 1.41 | 1.49 | 1.66 | 2.33 | 5.05 | 31.39 | 33.03 | 125.81
125.81
m³/s average at Kusum (Rapti basin), about 3.8 times Belsot, the next highest
Belsot (Kamala) and Chameliya/Nayalbadi (Mahakali) average about 31 to 33 m³/s.
Bhada Bridge is lowest at 0.70 m³/s. Averages cover the whole period.
Notes: Average discharge is very different between stations, which is why station information was kept as a model input (one-hot encoded) and why high flow was defined separately for each station.

## Slide 6: Highest discharge in July to September
Chart: Average discharge by month, all stations and years (m³/s)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Avg discharge | 4.31 | 3.8 | 3.53 | 3.2 | 3.25 | 6.31 | 53.72 | 72.46 | 52.97 | 28.61 | 8.74 | 5.05
72.46
Highest: August (m³/s)
Jul to Sep
Highest months, matching Nepal's monsoon season
3.20
Lowest: April (m³/s)
Notes: The monthly averages pool all stations and years, so high-discharge stations such as Kusum influence them strongly. The July to September rise matches the monsoon season.

## Slide 7: Same-day weather correlations are weak
Chart: Correlation with same-day river discharge
| Wind gusts (max) | Wind speed (max) | Precipitation | Rain | Humidity | Temperature | Dew point
Correlation | -0.0095 | 0.0516 | 0.0986 | 0.0997 | 0.1717 | 0.1785 | 0.2263
Strongest: dew point, r = 0.226
Weather variables showed relatively weak same-day linear correlations with discharge.
Historical and rolling features were included to capture temporal information.
Notes: These are Pearson correlations, so they only measure linear association on the same day. They do not show causation, and a weak same-day correlation does not by itself prove a delayed effect. I added lag and rolling features so the models could use earlier information.

## Slide 8: Feature engineering
Rain lags
Rain 1, 2 and 3 days earlier
Rolling rainfall
3-day and 7-day averages
Discharge lags
Discharge 1, 2 and 3 days earlier
Date features
Year, month and day
Station encoding
One-hot encoding of 10 stations
Regression target
Next day's river discharge
Linear Regression: without vs with engineered features
R²
0.8920
0.9038
RMSE
19.30
18.22
MAE
6.96
6.66
Errors fell: RMSE by 5.6%, MSE by 10.9% and MAE by 4.4%. RMSE and MAE are in m³/s.
Notes: I kept the same Linear Regression model and compared it with and without the engineered features, using the same chronological test set. All error measures improved and R-squared rose from 0.8920 to 0.9038. This comes from a single chronological split.

## Slide 9: Chronological train-test split
Training: first 80% of dates
10,710 records (1,071 dates), before 7 Dec 2025
Testing: last 20%
2,680 records
Cutoff date: 7 December 2025
Method
Dates were sorted and split at the 80% point, so every station shares one cutoff.
Purpose
A chronological split evaluates performance on later observations and reduces the risk of future-data leakage.
Limitation
One split only. Missing values were filled with full-dataset means, so leakage risk is reduced, not removed.
Notes: The counts and cutoff come from the final executed notebook: 1,339 unique dates, split at index 1,071, cutoff 7 Dec 2025, giving 10,710 training and 2,680 test records. A time-based split tests the model on later observations and reduces the risk of future-data leakage. It does not remove every risk: the mean used to fill missing values was calculated on the full dataset, and I used only one split.

## Slide 10: Regression model comparison
Model | MAE (m³/s) | MSE | RMSE (m³/s) | R²
Linear Regression | 6.66 | 331.87 | 18.22 | 0.9038
Random Forest | 2.88 | 510.17 | 22.59 | 0.8521
Decision Tree | 3.44 | 792.08 | 28.14 | 0.7704
Best value in each column is shown in teal. All models predict next-day discharge on the chronological test set.
Linear Regression
Highest R² (0.9038) and lowest RMSE (18.22 m³/s) of the three models.
Random Forest
Lowest MAE (2.88 m³/s), but a higher RMSE than Linear Regression. Decision Tree had the lowest R².
Limitations
Linear Regression sometimes predicted negative discharge, which is not physically possible. Extreme flows remain hard to predict.
Notes: Linear Regression was selected as the best regression model because it had the highest R-squared and the lowest MSE and RMSE. RMSE gives more weight to large errors. It is not best on every metric: Random Forest has the lowest MAE. Linear Regression also produced some negative predictions.

## Slide 11: Prediction errors and station-wise performance
Actual vs predicted: Linear Regression, test set
Dashed line = perfect prediction. Larger misses occur at high flows.
Chart: Linear Regression: MAE by station code (m³/s)
| 446.22 | 120 | 610 | 291 | 550.05 | 280 | 595.5 | 450 | 695 | 375
MAE | 2.99 | 3.37 | 3.66 | 4.1 | 4.19 | 4.34 | 4.55 | 5.06 | 5.15 | 29.15
Station 375 is the hardest to predict: average error 29.15 m³/s versus 2.99 to 5.15 at the other nine stations.
Notes: The scatter plot is Linear Regression on the test set. Points on the dashed line are perfect predictions. Station 375 is far harder than the others. One point on the plot sits far above the line, at an actual value of about 20 m3/s with a prediction of about 517 m3/s. The notebook filled missing target values with the mean, so I would treat that single point cautiously. I have not confirmed whether it is one of the filled rows.

## Slide 12: Regression: important predictive features
Chart: Permutation importance, Linear Regression (top 8)
| Precipitation | Rain | 3-day rolling rain | Station code | Longitude | Discharge (2 days earlier) | Discharge (1 day earlier) | Discharge (current day)
Importance | 0.0218 | 0.0298 | 0.0319 | 0.0378 | 0.0417 | 0.2025 | 0.3496 | 2.229
Reading the chart
Current and earlier discharge had the highest importance scores, far above rainfall and weather variables.
Rolling rainfall, rain and precipitation had smaller scores.
Importance shows which variables contribute to the model's predictions. It does not establish causation.
Notes: Permutation importance shuffles one feature on the test set and measures how much the model score drops. Current-day discharge is the input from day t used to predict day t+1, and the two earlier discharge values come next. Longitude and station code act as station identifiers. Importance describes what the model uses, not cause and effect.

## Slide 13: Classification of high-flow observations
Chart: Test-set metrics for high-flow classification (%)
| Accuracy | Precision | Recall | F1-score
Logistic Regression | 84.4 | 29.15 | 100 | 45.14
Decision Tree | 92.65 | 44.86 | 63.37 | 52.53
Random Forest | 95.75 | 72.31 | 54.65 | 62.25
Target definition
High flow = same-day discharge above the station's 90th percentile (from the training period). Features exclude same-day discharge but include earlier discharge.
Class imbalance
Training: 1,067 high-flow vs 9,643 other (10.0%). Test: 172 of 2,680 (6.4%). Class weights change each class's influence in training; the class counts stay the same.
Notes: This is classification of high-flow observations, not a next-day forecast. The label comes from the same day's discharge compared with a station-specific threshold. Class weights make the minority class count more during training but do not change how many observations are in each class.

## Slide 14: Classification performance and features
Random Forest confusion matrix
2,472
True negatives
36
False positives
78
False negatives (missed)
94
True positives
Random Forest misses 78 of 172 high-flow observations (recall 54.65%), with precision 72.31%.
Logistic Regression: recall 100%, but 418 false positives.
Chart: Important predictive features: Random Forest (top 8)
| 3-day rolling rain | Discharge (3 days earlier) | Soil moisture | Discharge (2 days earlier) | Month | Discharge (1 day earlier) | Dew point | 7-day rolling rain
Importance | 0.0514 | 0.0548 | 0.0615 | 0.0664 | 0.0913 | 0.1068 | 0.1209 | 0.1265
For flood alerts, the choice depends on the trade-off between missed high-flow events and false alarms. Feature importance shows what the model uses, not what causes high flow.
Notes: Random Forest has the best accuracy, precision and F1-score, but it misses 78 of the 172 high-flow observations. Logistic Regression catches all of them but raises 418 false alarms. The better choice depends on whether missed events or false alarms cost more. The feature chart shows what the model uses, not what causes high flow.

## Slide 15: Conclusions, limitations and future work
Key findings
Discharge was highest from July to September, peaking in August (72.46 m³/s average).
Linear Regression had the highest R² (0.9038) and lowest RMSE (18.22 m³/s); Random Forest had the lowest MAE (2.88 m³/s).
Feature engineering improved Linear Regression (RMSE 19.30 to 18.22 m³/s).
Random Forest classification: 95.75% accuracy, 72.31% precision, 54.65% recall. Logistic Regression: 100% recall.
Limitations
Extreme flows are hard to predict, especially at Station 375
Linear Regression gave some negative discharge values
Missing values, including the target, were filled with the mean
Random Forest missed 78 of 172 high-flow observations
Classification is same-day, not a next-day forecast
One chronological split; new stations not tested
Possible future improvements (not done here)
Non-negative discharge predictions
Dam and upstream data
Better handling of missing values
Next-day high-flow classification
Notes: Summarise with the right confidence: strong next-day regression performance overall (R-squared 0.9038), weaker on extreme flows, and a classification trade-off between precision and recall. Be open about the limitations the notebook lists, especially mean-filled values. The future improvements are ideas, not completed work.